## Slide 1: RoboGen Project: Group 7
M. Hassan,
L. Zunino,
L. Duggan,
H. Sprumont,
MICRO-515 Evolutionary robotics
29.05.2022
Figure 1: Final image of robot body
Figure 2: Final image of robot body (real)

## Slide 2: Introduction: Mars exploration rover
Locomotion on uneven terrain
Stability of the core component →
Obstacle avoidance
Figure 3: Grand challenge arena
Scientific approach / Repeatability
Exploring the parameters of Robogen

## Slide 3: Experimental Method:
Figure 4 : Project flowchart

## Slide 4: Experimental Method: Starting robot
2 Random starts:
  More exploration
  Surprises !
Rolling snake:
  Oscillators only
  Good racing score
  Simple geometry
Starfish:
  Oscillators only
  Good racing score
  Advanced geometry
Figure 5 : Starting robots and one of our random results

## Slide 5: Experimental Method: Starting robots (bis)
Oscillators | LowerLeg1 | Hip1 | Hip2 | LowerLeg2
Period | 0.8 | 0.8 | 0.8 | 0.8
Offset | 0.2 | -0.8 | -0.95 | -1
Amplitude | 1 | 1 | 1 | 1
2 Random starts:
  More exploration
  Surprises !
Rolling snake:
  Oscillators only
  Good racing score
  Simple geometry
Starfish:
  Oscillators only
  Good racing score
  Advanced geometry
Figure 6 : Rolling snake core and actuators
Table 1 : Rolling snake oscillator parameters

## Slide 6: Experimental Method: Starting robots (bis)
Oscillators | Hip 1 | Hip 2 | Hip3 | Hip 4 | knee1 | knee 2 | knee 3 | knee 4
Period | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Offset | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
Amplitude | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
2 Random starts:
  More exploration
  Surprises !
Rolling snake:
  Oscillators only
  Good racing score
  Simple geometry
Starfish:
  Oscillators only
  Good racing score
  Advanced geometry
Table 3 : Brain-only Evolved Starfish
Table 2 : Starfish starting oscillator parameters
Oscillators | Hip 1 | Hip 2 | Hip3 | Hip 4 | knee1 | knee 2 | knee 3 | knee 4
Period | 1.87 | 2 | 1.83 | 2 | 1.92 | 1.99 | 1.61 | 2
Offset | 1 | -0.57 | -0.89 | 0.41 | 0.38 | 0.17 | 0.24 | 0.64
Amplitude | 1 | 0.83 | 0.78 | 0.93 | 1 | 1 | 1 | 1

## Slide 7: Experimental Method: Initial parameters
Figure 7 : Arena of evolutionary step 1
Table 5 : Simulation parameters
Motor noise | Sensor noise | Simulation time (s) | max direction shifts per second
0.03 | 0.03 | 12 | 16
Table 4 : Evolution parameters
Number of generations | 200
Mu | 25
Lambda | 100
Replacement strat | plus
Tournament size | 3
pBrainMutate | 0.5
BrainSigma | 0.9

## Slide 8: Experimental Method: Locomotion
Racing (Final distance of the closest element)
Minimum distance + Stability
Integral of Core position
Final Core position
Final Core position + Stability
A variety of fitness functions:

## Slide 9: Intermediate results: Random configuration
Figure 8: Fitness evolution: Max (x,y) distance + max acceleration, roll, pitch fitness function
Figure 9 : Robot at the end of the evolution

## Slide 10: Intermediate results: Snake and starfish
GorillaBot :
Starfish:
↑ ↑
Figure 10 : GorillaBot and Starfish in simulation
(Don’t judge them, they’ve been through a lot)
← Figure 11 : Fitness evolution for both robots →

## Slide 11: Experimental Method: Obstacle avoidance
Brain evolution, manual sensor placement:
  Fitness functions:
Figure 12 : Arena for implicit obstacle avoidance
Body and brain evolution, implicit OA:
  Fitness function: Racing scenario with conditions on minimum number of sensors and no obstacle removal
  Constant battle with the robot’s exploits (no IR sensors on robot, obstacle despawning, lucky starting position, ...)
1.
2.

## Slide 12: Results
Figure 13 : Fitness evolution : Brain-only OA fitness function
Figure 14 : Robot at the end of the evolution

## Slide 13: Results
Figure 15 : Fitness evolution : Brain-only OA fitness function
Figure 16 : Robot at the end of the evolution

## Slide 14: Results
Figure 17 : Fitness evolution : Brain-only OA fitness function
Figure 18 : Robot at the end of the evolution

## Slide 15: Video of GorillaBot - Simulation (2x speed)

## Slide 16: Video of GorillaBot - Real robot

## Slide 17: Conclusion
Observations
Simpler fitness functions worked better
Random start has greater variability in results
Repeatability is more guaranteed with non-random start configurations (GorillaBot: obtained ⅖ times)
Evolutionary algorithm is opportunistic
Future works, if we had more time :
  Longer evolution with more starting positions
  Explore more the implicit OA (tweaking arenas, …)
  More random starts (funny results)
  Train on different arena for more general results
Figure 19 : Artistic depiction of GorillaBot

## Slide 18: Workload distribution
 | M. Hassan | L. Zunino | L. Duggan | H. Sprumont
Starting robot | Starfish | Random | Random | Snake
Final OA | Starfish + Gorilla | Random |  | Gorilla
Robot build |  |  | Body + Sensors | Body